## Slide 1: 3DFormer: Enhancing Snapshot Compressive Imaging Performance with 3D Gaussian Splatting
Penghao Yin
2025.1.2
Notes: Hello everyone, I’m Yin Penghao, and I will report the progress in my graduation project. The topic of my representation is 3DFormer: Enhancing Snapshot Compressive Imaging Performance with 3D Gaussian Splatting.

## Slide 2: Content
Introduction of SCI
Introduction of 3D Reconstruction and Rendering
My Effective Improvements
Experimental Results
Future Expectation
Notes: My presentation will include 5 main parts. First of all, I will introduce the necessary background information of Snapshot Compressive Imaging. By the way, in the following representation, I will use SCI to refer to Snapshot Compressive Imaging. After that, I will show you the limitations of traditional SCI methods, and address these issues with 3D reconstruction and rendering. The third part will be my effective improvements among all of my experiments based on the previous SOTA method. The improved method reached better results, which will be shown in the fourth part. The last part will be my expectation of future work.

## Slide 3: Content
Introduction of SCI
Introduction of 3D Reconstruction and Rendering
My Effective Improvements
Experimental Results
Future Expectation
Notes: The first part is the introduction of SCI.

## Slide 4: Introduction of SCI
SCI Model
Measured Image
Masks
Original Video Frames
Detail of Masks
?
Notes: SCI is an innovative imaging technique that enables the simultaneous compression and reconstruction of images during a single exposure. It utilizes a single piece of measured image and a series of given masks to generate original video frames. (click) Each mask is a matrix consisted of value 0 and 1. (click) But how can we obtain the measured image? In fact, when taking video, the camera shifts the mask with a very high frequency during a shutter time, and each mask maintains the same duration. Then the measured image of the camera will be the measured image shown in this slide.

## Slide 5: Introduction of SCI
Masks
Original Video Frames
Measured Image
Notes: According to the principles mentioned just now, the measured image can be modeled as the sum of the element-wise product of corresponding original video frames and masks. In other words, we can use mathematical equations to represent this process.

## Slide 6: Introduction of SCI
Let denote measured image, original video frames and masks respectively, are the number of frames, image height and image width. The process of SCI can be represented as the mathematical form as follows:
For colored video with channels, . We first copy for times, that is , as the same pixel shares the same value of mask. We can also represent the process in the following equation:
Notes: (陈述PPT)

## Slide 7: Previous SCI Methods
Classification of previous methods:
Optimization-Based Models (Not frequently used nowadays):
  Modeling the SCI problem as an optimization problem and solving it using methods such as ADMM (Alternating Direction Method of Multipliers).
Deep Plug-and-Play Models:
  Using deep neural network to substitute the priors of traditional optimization models.
Deep Unfolding Networks:
  Unfolding deep plug-and-play models to construct an end-to-end network. The forward process of this network is similar to deep plug-and-play models.
End-to-End Networks:
  Leveraging networks that have proven effective in other image processing tasks, such as CNN, Transformer and diffusion models, to develop a network for SCI image restoration.
Classification | Representative Methods
Deep Plug-and-Play Models | PnP-SCI (CVPR, 2020), PnP-SCI_python (TPAMI, 2022)
Deep Unfolding Networks | SCI3D (ICCV, 2021), ELP-Unfolding (ECCV, 2022), CTM-SCI (ICCV, 2023), GAP-net (IJCV, 2023), DPU (CVPR 2024)
End-to-End Networks | STFormer (TPAMI, 2022), DiffSCI (CVPR, 2024), MambaSCI (NeurIPS, 2024)
Notes: In the region of SCI, there are a lot of previous SCI methods. We mentioned just now that the process of SCI can be modeled as equations. However, the equation is ill posed, as the dimension of original video is larger than the measured image. The earliest methods are optimization-based. In these kind of methods, researchers model the SCI problem as optimization problems by adding different priors, and solve them using methods such as ADMM. As the hand-craft priors are too simple to capture all the features of the original video, these methods usually show sub-optimal results and are not frequently used nowadays. To build more complex priors, researchers use deep neural network to substitute the priors of traditional optimization models, which are concluded as deep plug-and-play models. After that, researchers seek for end-to-end networks to solve the SCI problem, so they raised deep unfolding networks, which unfolds deep plug-and-play models to construct an end-to-end network. The forward process of this kind of network is similar to deep plug-and-play models. And as the popularity of powerful network structures such as CNN, Transformer and diffusion models and the improvement of computational resources, scientists also modify the networks that have been proven effective in other image processing tasks to solve the SCI problem.
The following table lists some representative methods of deep plug-and-play models, deep unfolding networks and end-to-end networks. They provide inspirations for my work.

## Slide 8: Content
Introduction of SCI
Introduction of 3D Reconstruction and Rendering
My Effective Improvements
Experimental Results
Future Expectation
Notes: The second part is the introduction of 3D Reconstruction and Rendering.

## Slide 9: Limitation of Traditional Methods
The traditional deep learning-based SCI methods often fall short in effectively modeling the physical properties of objects, such as shape, texture and color, in video scenes.
The result of STformer (deep learning-based methods)
The result of our method
False Rendering of Color
Inefficient Detail of Texture
Distorted geometric shape
Notes: Before introduction, it’s a good question that why do we need to introduce 3D? That’s because there exists limitation of traditional methods. The traditional deep learning-based SCI methods often fall short in effectively modeling the physical properties of objects, such as shape, texture and color, in video scenes. We compare the result of a traditional method named STFormer and ours. (click) The purple rectangles show that the result of traditional methods lack efficient details of feature. (click) The yellow rectangles show there exists distorted geometric shapes in the output of traditional methods. (click) The red rectangles show that the traditional methods will output false rendering of color. Solving these problems is important for raising the accuracy of SCI.

## Slide 10: Limitation of Traditional Methods
How to solve these problems?
Perhaps we can leverage 3D reconstruction and rendering techniques. In 3D scenes, objects are represented by a finite set of basic elements, meaning that 3D scenes themselves are low-dimensional. Since the real world is also inherently low-dimensional, applying 3D reconstruction and rendering can address issues such as blurred textures, distorted shapes, and unrealistic colors, which are typically high-dimensional phenomena.
The 3D scene constructed in our method
Notes: But how to solve them? Perhaps we can leverage 3D reconstruction and rendering techniques. In 3D scenes, objects are represented by a finite set of basic elements, meaning that 3D scenes themselves are low-dimensional. Since the real world is also inherently low-dimensional, applying 3D reconstruction and rendering can address issues such as blurred textures, distorted shapes, and unrealistic colors, which are typically high-dimensional phenomena.

## Slide 11: Structure from Motion
Structure-from-Motion (SfM) is a widely used computer vision technique that aims to recover the 3D geometric structure of a scene and the motion of the camera from a series of 2D images, which are inputs for 3D reconstruction. The core steps of SfM are briefly as follows：
feature extraction and matching
camera pose estimation
3D reconstruction
optimization using additional images
Popular SfM frameworks include OpenMVG (RRPR, 2016), COLMAP (CVPR, 2016 and ECCV, 2016), VGGSfM (CVPR, 2024), and others.
Structure from Motion Models
Input images (more than one)
Output 3D point clouds and camera poses
Notes: OK. As we want to use 3D reconstruction and rendering methods to address SCI problem, we need to know its process first. Structure-from-Motion (SfM) is a widely used computer vision technique that aims to recover the 3D geometric structure of a scene and the motion of the camera from a series of 2D images, which are inputs for 3D reconstruction. In other words, we input a series of images of the same scene to the Structure from Motion model, we can obtain the 3D point clouds of the scene and the camera pose of each image.

## Slide 12: 3D Reconstruction and Rendering
3D Scene Reconstruction and Rendering aims to recover the three-dimensional structure of a real-world scene from a set of input images, and render the captured images from the perspective of arbitrary camera poses, with the camera’s intrinsic and extrinsic parameters and the original sparse point clouds provided.
The mainstream methods include NeRF (ECCV, 2020) and 3D Gaussian Splatting, i.e. 3DGS (SIGGRAPH, 2023).
Structure of NeRF
Structure of 3DGS
Notes: With the images of a scene, and the camera poses and point clouds produced by SfM models, we can use 3D Scene Reconstruction and Rendering methods to recover the three-dimensional structure of the scene. After that, we can render the captured images from the perspective of arbitrary camera poses, with the camera’s intrinsic and extrinsic parameters and the original sparse point clouds provided. The mainstream methods include NeRF and 3D Gaussian Splatting, also 3DGS.

## Slide 13: 3D Reconstruction and Rendering
 | NeRF | 3DGS
Basic Element | Neural Radiance Field | 3D Gaussian Point Cloud
Advantages and Disadvantages | Provide high-quality results Requires significant training time | Provide higher-quality results Improve computational efficiency
Comparation between NeRF and 3DGS
According the table, 3DGS demonstrates better performance in 3D reconstruction and rendering tasks.
However, 3DGS also has limitations, such as its need for good initialization and the quality of rendering. To address these limitations, Kheradmand et al introduced 3DGS-MCMC (NeurIPS, 2024), which further enhances both rendering quality and computational efficiency.
Notes: NeRF uses neural radiance fields to represent 3D scenes, while 3DGS uses 3D Gaussian point cloud. This difference contribute to there difference in performance. Compared with NeRF, 3DGS is superior for higher-quality results and improved computational efficiency. However, 3DGS also has limitations, such as its need for good initialization and the quality of rendering. To address these limitations, Kheradmand et al introduced 3DGS-MCMC (NeurIPS, 2024), which further enhances both rendering quality and computational efficiency.

## Slide 14: Previous Work Based on 3D
SCINeRF
Based on NeRF
SCISplat
Based on 3DGS-MCMC
Notes: Based on NeRF and 3DGS, previous researchers designed several models for SCI task, such as SCINeRF, SCIGS and SCISplat.

## Slide 15: Previous Work Based on 3D
Initialization
SfM
3DGS-MCMC
Notes: I want to introduce SCISplat in detail, as it is the basis of my work. There are 3 main process in SCISplat. (click) The first process is initialization. SCISplat utilizes the measured image to calculate the values of pixels in original video where the corresponding value of mask is non-zero, and fills in other pixels using interpolation. (click) After that, this method input the interpolated images to structure-from-motion methods to get point clouds and corresponding camera poses. (click) Finally, SCISplat input the interposlated images along with the point clouds and camera poses to 3DGS-MCMC model to build a 3D scene, and render the images from the camera poses of interpolated images. The rendered images will work as the reconstructed original video of the SCI process. The loss function of 3DGS-MCMC includes the consistency loss between synthesized measurement calculated from rendered images and real measurement.

## Slide 16: Content
Introduction of SCI
Introduction of 3D Reconstruction and Rendering
My Effective Improvements
Experimental Results
Future Expectation
Notes: The third part is my effective improvents.

## Slide 17: Outline of My Model
1. Introduce STFormer
2. Modifying Loss
SCISplat
Ours
Notes: Compared with SCISplat, our model has 2 main changes. First, we introduce STFormer to get original reconstructed images, rather than simple interpolation. Second, we modified the loss used for 3DGS-MCMC.

## Slide 18: Introducing STFormer
Structure of STFormer
Since 3D reconstruction and rendering requires images from multiple perspectives as input, we first feed the measured SCI image and corresponding masks into the STFormer module to generate the reconstructed images. The reconstructed images are then used as the good input for SfM model.
Notes: Spatial-Temporal Transformer (STFormer) is an end-to-end network designed for SCI. Its core component is the STFormer block, which leverages both spatial and temporal self-attention mechanisms to capture the relationships between adjacent tokens in videos. This allows the model to effectively model both spatial dependencies within individual frames and temporal dependencies across frames. The structure of STFormer is illustrated in the figure above. Since 3D reconstruction and rendering requires images from multiple perspectives as input, we first feed the measured SCI image and corresponding masks into the STFormer module to generate the reconstructed images. The reconstructed images are then used as the good input for SfM model.

## Slide 19: Modifying Loss
Previous research has not fully utilized the output of STFormer to designate loss function.
Loss in SCISplat
My Modified Loss
This modification is proved to enhance the low-frequency signals and reduce noise and artifacts in the reconstructed images.
Notes: After that, we observed that the measured images retain sufficient high-frequency components but lack low-frequency components. As a result, previous methods often introduce significant noise. Since the original reconstructed images produced by VGGSfM exhibit good quality in the low-frequency range, we use them to enhance the low-frequency signals and reduce noise and artifacts in the reconstructed images. Previous research has not fully utilized the output of STFormer to designate loss function, so we added the consistency loss between rendered images and the output of STFormer. This modification is proved effective.

## Slide 20: Content
Introduction of SCI
Introduction of 3D Reconstruction and Rendering
My Effective Improvements
Experimental Results
Future Expectation
Notes: In the fourth part I will show my experimental results.

## Slide 21: Qualitative Results
Ground Truth
SCINeRF
STFormer
Ours
Qualitative results show that our method produces visually superior reconstruction results than others.
Besides, compared with the outputs of STFormer, the results demonstrate that 3DGS-MCMC significantly improves the SCI reconstruction quality.
Notes: First I will show qualitative results. The images show that our method produces visually superior reconstruction results than others. The output of our method has less noise and more details. Besides, compared with the outputs of STFormer, the results demonstrate that 3DGS-MCMC significantly improves the SCI reconstruction quality.

## Slide 22: Quantitative Results
Qualitative Results on dataset airplants
As SCISplat’s code is not open-sourced, its quantitative results are obtained from the paper.
Quantitative results on the airplants dataset show that our method 3DFormer reaches state-of-the-art performance in all indexes.
Notes: After that, I want to show quantitative results. In the table, the first 3 indexes, PSNR, SSIM and LPIPS shows the consistency between output images and ground truth, and the last three indexes, MUSIQ, MANIQA and CLIPIQA represent the image quality without the ground truth. According to the table, our method 3DFormer reaches state-of-the-art performance in all indexes.

## Slide 23: Content
Introduction of SCI
Introduction of 3D Reconstruction and Rendering
My Effective Improvements
Experimental Results
Future Expectation
Notes: Finally, I will briefly introduce my future expectation.

## Slide 24: Future Expectation
1. Improving STFormer:
  STFormer requires significant memory, making it less hardware-friendly for small devices like cameras. We aim to replace it with a more lightweight architecture, enabling its deployment on portable devices.
2. Enhancing 3DGS-MCMC:
  The 3DGS-MCMC method can be further improved to create more realistic physical scenes. Recent works have enhanced the original method by modifying the modeling of 3D Gaussian point clouds or adjusting the loss functions. These approaches can provide valuable insights for improving our model.
3. Reducing Training Time:
  The training process of 3DGS-MCMC is computationally expensive and time-consuming. We aim to eliminate unnecessary steps in the process to speed up training and improve efficiency.
Notes: We will improve our model in 3 main fields. First, we want to Improve STFormer. As STFormer requires significant memory, making it less hardware-friendly for small devices like cameras, we aim to replace it with a more lightweight architecture, enabling its deployment on portable devices. Second, we will enhance 3DGS-MCMC. We believe that the 3DGS-MCMC method can be further improved to create more realistic physical scenes. And recent works have provided valuable insights, such as modifying the modeling of point clouds or adjusting the loss functions, for improving our model. Third, we want to reduce training time by eliminating unnecessary steps in the 3DGS process to speed up training and improve efficiency.

## Slide 25
THANK YOU!
Notes: OK, that’s all of my introduction for my progress in graduation project. Thank you for your listening!